## Slide 1: Interconnected Mini-grids for rural energy Transition A Case of Nepal
Binod Prasad Koirala1, Alexander Schies1, Brisa Ortiz1, Tilak K. Limbu2 and Bhupendra Shakya2
1Fraunhofer Institute for Solar Energy Systems ISE, Freiburg 2Alternative Energy Promotion Center (AEPC), Nepal
Micro Perspective of Decentralized Energy Supply Conference 28.02.2013, Berlin
www.ise.fraunhofer.de

## Slide 2: Outline
Fraunhofer ISE and AEPC
Introduction
Socio-Political Relevance
Next Generation of Renewable Based Mini-grids
Cases: Baglung and Nawalparasi Mini-grids
New Project: Renewable Based Interconnected Mini-grids
Conclusions

## Slide 3: Fraunhofer-Institute for Solar Energy Systems ISE
Largest European solar energy research institute
ca. 1200 members of staff (incl. students)‏
Areas of business:
Photovoltaics (Si, CPV, OPV)
Solar Thermal (ST, CST)
Renewable Power Generation
Energy-Efficient Buildings and
Technical Building Components
Applied Optics and Functional
Surfaces
Hydrogen Technology
10% basic financing 90% contract research 50% industry, 40% public € 69 M total budget (‘11) > 10% p.a. growth rate
Source: Eicke R. Weber, International Conference on Microtechnology, IMTEK (Freiburg), 11 October 2012

## Slide 4: Autonomous System and Mini-Grids
Business Areas:
  Socio-economic/socio-technical analyses
  Consulting, promotion, training
  Implementation strategies, financing concepts
  Development, testing and optimizing of components
  Development of operating strategies, energy and battery management systems
  Demonstration projects, system monitoring and quality assurance

## Slide 5: AlterNATIVE Energy Promotion Center (AEPC)
Nodal government agency established in 1996
Making Renewable Energy mainstream supply to rural areas of Nepal
Main role and responsibilities:
  Short, medium and long term policy and plan formulation
  Promotion of RET development programmes
  Standarization, quality assurance and monitoring
  Subsidy and financial assistance delivery
  Co-ordination of various government org., Donor, IGO/INGO, private
National Rural Renewable Energy Program (2012- 1017)

## Slide 6: Introduction
> 2 billion population have no access or no reliable access to electricity
99 % of these population are in developing countries
4 out of 5 lives in rural areas
In Nepal
  56 % population has access to electricity ( 49 % - rural areas)
  Upto 16 hours of load-shedding in National Grid
Individual renewable energy technologies: socio-economic benefits??
Integrative and modular interconnected mini-grids: Productive use

## Slide 7: Socio-Political Relevance
Universal access to modern energy services by 2030
2012 – International year of Sustainable Energy for all
2014-2024 – Decade for Sustainable Energy for all
Energy access – MDGs / post-2015 agendas
Basic energy access vs. Enhanced energy access
Energy access: Improves essential services (health, communication education)
Migration problem

## Slide 8: Next Generation of Renewables Based Mini-Grids
Upto 1 MW
Distributed generation
LV or MV integration
Advantages
  Grid Stabilization
  Reliable energy supply
  Avoids end-user maintenance
  Periodic maintenance
©Fraunhofer ISE

## Slide 9: Next Generation of Renewables Based Mini-Grids
Simple integration of different energy sources (PV, wind, hydro, etc.)
Least-cost option
Increasing quality of energy services
Support local infrastructure and economic development
Alternative solution to the national electrical grid
61

## Slide 10: Case 1: Baglung Mini-grids
Interconnected Micro-hydro Mini-grids Project (2011)
  Baglung district, Nepal
  Funded by UNDP and World Bank
  Technical support from RERL and AEPC
  7 MHP plants (132 kW)
    Kalung Khola I and II (12 and 22 kW) Urja khola I,II,III and IV ( 26, 9, 25 and 14 kW) Theule Khola MHP ( 24 kW)
  8 km, 11 kV transmission lines
  1200 Households
  Urja Upatakya Mini-grid co-operatives
  Individual power producers

## Slide 11: Positive Effects
Social
  Awareness about project
  Decreased misuse
  End use in income generation
  Inter community co-ordination
  Increase confidence level
  Follow rules and regulations
  Mini-grids – social entity for generation, transmission and distribution of rural energy
Technical
  Stable voltage and frequency
  Upgraded service reliability
  24 hrs availability
  Soft starting of motor possible
  Load sharing between Gen.
  Improved fault detection process
  Capacity building of operators
  End use ( 15 kW communication tower, 40 hp stone crusher)
© RERL

## Slide 12: Case 2: PV- Wind Hybrid Mini-Grids
PV-wind Hybrid Mini-grids (2011)
  2 × 5 kW wind turbines
  2 kWp solar PV
  43.5 kWh/day
  46 Households
  Rural Energy service company
  Hoorhoore Danda co-operative
Financed by ADB
Technical support from AEPC
©AEPC

## Slide 14: Demand Forecast and Energy Generation
61
© AEPC /ADB

## Slide 15: New Project: Renewable Based Interconnected Mini-grids
Interconnected Mini-grids for Intensive Rural Electrification in Nepal (IMIREN)
Development co-operation project between Fraunhofer ISE and AEPC
Basic funding from WISIONS initiative, Sustainable Energy Project Support (SEPS) Wuppertal Institute, Germany
Co-financing from Fraunhofer ISE and AEPC
First phase interconnection of:
  Daram Khola MHP (70 kW)
  Paropakar MHP ( 116 kW)
Second Phase: interconnection of other RE

## Slide 16: Project Details
Paropakar MHP
  116 kW
  1200 Households
  Excess generation
  Community Owned
Daram Khola MHP
  70 kWp
  700 Households
  Overloaded
  Privately Owned
Regulatory Framework
Dissemination Workshop

## Slide 17: Project Site

## Slide 18: Conclusion
Renewable energy access for billions of people has recently become global priority
Basic energy access vs. enhanced energy access
Interconnected Mini-grids transitions
Multiplier effects: Business and Operation Models, Demonstration Projects
Future village energy supply: Renewables based Interconnected Mini-grids

## Slide 19: Thank you very much for your attention! Questions???
Fraunhofer Institute for Solar Energy Systems ISE
Binod Prasad Koirala
www.ise.fraunhofer.de
bkoirala@ise.fraunhofer.de
Notes: Bild: ISE Hauptgebäude
Bild, Multikristalline Silicium Solarzelle
Bild, >99% Wechselrichter
Hagelteststand (Solarthermie)
Heizölbetriebener Gasbrenner